## Slide 1: Bluetooth Low Energy Peripherals
A Primer and Demo

## Slide 2: Introduction – Steven Knudsen
B.Sc. Computer Engineering 1984 U of A
M.Sc. Applied Sciences in Medicine 1987 U of A
Ph.D. Electrical Engineering 1993 U of C
P.Eng. APEGA
5 startups, 2 as co-founder
Lecturer, Professor, Researcher (Wissenschaftlicher Mitarbeiter)
Jr./Sr./Chief Engineer, VP Engineering, CTO
Consultant
Software, Hardware, Algorithms
Boundary Problems
Notes: signal processing signal processing signal processing signal processing signal processing signal processing ubiquitous IoT ubiquitous IoT ubiquitous IoT pervasive pervasive pervasive RF RF SDR SDR SDR SDR radiofrequency NMR MRI satellite imaging imaging mathematics programming programming Arduino Arduino Raspberry Pi Raspberry Pi Raspberry Pi Onion Photon Duo Electron Java C C++ ObjC Swift Java Linux Linux Linux OSX OSX iOS iOS iOS Android Android embedded Wifi 802.11 802.11 Bluetooth

## Slide 3: Main Topics

## Slide 4
BLE basics
  Central and Peripheral roles
  Client and Server roles
  Services and Characteristics
  SIG-defined services, etc.
Example
  Hardware (Peripheral) to accept data
  iOS App (Central) to access the peripheral
Q&A

## Slide 5: Bluetooth Low Energy Basics

## Slide 6: Bluetooth Low Energy (BLE)
Extension to Bluetooth 4.0, but not really like the main spec
  Think of as a light-weight subset of Bluetooth
  Not meant for transferring a lot of data
  Developed independently of Bluetooth as in-house Nokia project; “Wibree”
Designed to support very low power applications
  Small battery-powered devices that do not require much data or frequent transfers

## Slide 7: Example device - MbientLab
Motion tracker
  accelerometer + gyroscope
  barometer + temperature
  magnetometer
  ambient light sensor
Peripheral queried by phone or other BLE “Central”
Notes: Findability applications – Tile
Beacons – provide a small amount of location-specific info

## Slide 8: Primary Use Case – Simple Info
I’m here!
I’m here!

## Slide 9: Device discovery
Heard you.
Can we talk?

## Slide 10
Sure.

## Slide 11: Service discovery
I see your services. Tell me more about that one.

## Slide 12: Service characteristics inquiry
It has these characteristics

## Slide 13: Data exchange
Great.
Give me the data for that characteristic.

## Slide 14
Here you go…

## Slide 15: Transactional
Thanks.
Goodbye.
23C
97 kPa

## Slide 16: Independence
I’m here!
I’m here!

## Slide 17
https://devzone.nordicsemi.com/documentation/nrf51/5.2.0/html/modules.html
Notes: Sure, could have shown all the previous slides more succinctly with a message sequence chart, but that’s boring and probably has too much detail.
That said, there are lots of great online resources including this one by Nordic Semiconductor, who make the very popular and capable nRF series of transceivers.

## Slide 18: States and Actions
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Notes: Idle – standing by, Bluetooth may be turned on, but not active. May even be in a deep sleep state
Discovery – where peers find each other, by scanning, advertising, or alternating both
Connection – two peers have a mutual interest and connect to pass on or exchange data

## Slide 19: States and Actions - Idle
Central
Peripheral
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Notes: We tend to think of the peripheral as the less capable device, but

## Slide 20: States and Actions - Idle
Peripheral
Central
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Notes: Nothing says it has to be so. A device can be what it wants when it wants.

## Slide 21: States and Actions – Device Discovery
Central
Peripheral
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Notes: In device discovery, the Central scans for peripherals, which are advertising their availability.

## Slide 22
Notes: Advertise on up to 3 channels spaced to avoid the most used WiFi channels.
Usually set up to advertise on all three, hopping between them at prescribed intervals.

## Slide 23: States and Actions – Connection
Client
Server
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Request
Response

## Slide 24: States and Actions – Connection
Client
Server
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Notify (with or without data)
Notify (with or without data)

## Slide 25: States and Actions – Connection
Client
Server
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder
Read 20 bytes at a time
Notify – have N bytes of data

## Slide 26: BLE Stack
Controller
Host
App
Applications
Host Controller Interface (HCI)
Link Layer (LL)
Physical Layer (PHY)
Direct Test Mode
Logical Link Control and Adaptation Protocol (L2CAP)
Attribute Protocol (ATT)
Generic Attribute Profile (GATT)
Generic Access Profile (GAP)
Security Manager

## Slide 27: GAP – Generic Access Profile GATT – Generic Attribute Profile
GAP defines the general topology of a network.
Central
Peripheral
GATT describes how attributes are organized for transfer once devices are connected
Client
Server

## Slide 28: GAP – Communication Mechanisms
Broadcasting
  Devices don’t have to connect
  Broadcaster transmits public advertising data packets with a small amount of data
  Observer listens for broadcast packets
Connecting
  More common that Broadcasting
  Devices connect and handshake to exchange data
  Peripheral advertises (beacons) so central devices can connect
  Central initiates connection after hearing beacon; can be refused by peripheral

## Slide 29: ATT – Attribute Protocol
Based on Client ⇔ Server relationship.
Server exposes a set of attributes to a client that are accessible using the attribute protocol
Attribute is a discrete value comprising
  Type defined by UUID. Short, 16 bit, for SIG-assigned. Long, 128 bit, for custom.
  Handle
  Permissions
Notes: The Generic Attribute Profile is based on the Attribute Protocol, so best to start with it.

## Slide 30: ATT – Attribute Protocol examples
Heart Rate Service | Handle | Type of attribute (UUID) | Attribute permissions | Attribute values
Service Declaration | 0x000C | Service declaration Standard UUIDservice 0x2800 | Read Only, No Authentication, No Authorization | Heart Rate Service 0x180D
Characteristic Declaration | 0x000D | Characteristic declaration Standard UUIDcharacteristic 0x2803 | Read Only, No Authentication, No Authorization | Properties (notify), Value Handle (0x000E), UUID for Heart Rate Measurement characteristic (0x2A37)
Characteristic Value Declaration | 0x000E | Heart Rate Measurement Characteristic UUID found in the Characteristic declaration value 0x2A37 | Higher layer profile or implementation specific | Beats Per Minute e.g. “167”
Descriptor Declaration | 0x000F | Client Characteristic Configuration Descriptor (CCCD) Standard UUIDCCCD 0x2902 | Readable with no authentication or authorization. Writable with authentication and authorization defined by higher layer specification or is implementation specific | Notification enabled 0x000X
Characteristic Declaration | 0x0010 | Characteristic declaration Standard UUIDcharacteristic 0x2803 | Read Only, No Authentication, No Authorization | Properties (Read), Value Handle (0x0011), UUID for Body Sensor Location (0x2A38)
Characteristic Value Declaration | 0x0011 | Body Sensor Location UUID found in the Characteristic declaration value 0x2A38 | Higher layer profile or implementation specific | Sensor Location (8-bit integer) e.g., 3 equals “finger”
Short, so standard from Bluetooth SIG
Permissions apply only to values
Values can be anything, including UUID or other info

## Slide 31: GATT
Profile
Service
Characteristic
Characteristic
Characteristic
Service
Characteristic
Characteristic
Descriptor
Descriptor

## Slide 32: Main Development Context
Central
Peripheral
Standby
Scanner
Initiator
Idle
Device Discovery
Connection
Advertiser
Responder

## Slide 33: Example

## Slide 34: Redbear.com BLE Nano
Nordic nRF51822 SoC supports both BLE Central and BLE Peripheral roles
Ultra low power consumption
Support voltage from 1.8V to 3.3V
Software development using mbed.org, GCC, Keil or Arduino

## Slide 35: Measured power consumption
24 µA average for 660 ms interval
CR2032 has 240 mAh
240000 µAh / 24 µA = 10,000 hours
416 days

## Slide 36: Peripheral/Server – BLE Nano
mbed.org is the development environment. Lots of examples – “BleNanoLed”
Advertises on a 100 ms interval
Defines one service with two characteristics
We use only one characteristic that accepts data without requiring an authorization, authentication, or a response
  Client writes up to 20 bytes at a time, but we need only one

## Slide 37
main.cpp
Device name is part of advertising info, i.e., local “data”

## Slide 38
Usual to have callbacks so that BLE managers can let the application do something interesting
No need to advertise when connected implied. Save power…

## Slide 39
End of main.cpp
Set up callbacks
Set up services
Low latency, but power draining
Events handled asynchronously in callbacks

## Slide 40
Service definition
Service and characteristics UUIDs definition
Can write to peripheral with no authentication, no authorization, and don’t need a response
Only allows notification
Defines service for base UUID + characteristics

## Slide 41
Write and read handlers
We will write to the TX characteristic. The value is parsed here…

## Slide 42
LED control

## Slide 43: iOS App
Main steps
  Listen for advertising peripherals
  Filter on device “BLENano”
  Connect to peripheral if match
  Confirm device has desired service and characteristics
  Use TX characteristic to control LED
Simple single-view app
Have to run on iPhone since simulator doesn’t do Bluetooth
https://github.com/knud/HackEDBLE

## Slide 44
My own wrapper for iOS Core Bluetooth
Make this the target for callbacks

## Slide 45
Should have progress indicator
Check for desired service
Confirm

## Slide 46
Confirmed! Get characteristics
If TX characteristic, we are in business

## Slide 47: Demo

## Slide 48: Q&A
Notes: Here are two examples that are pretty simple, but solve real world problems, and can be done using the tools we have here today.